## Slide 1: Porting Micrium OS to Nucleo-F446RE

## Slide 2: Table of contents
Introduction | Briefly introduce the project goal & the tools used
Nucleo-F446RE Setup | configure for Nucleo-F446RE by utilizing Board Support Package (BSP) & interfacing with the HAL layer.
Porting Micrium OS | Configuring Micrium OS to work with the specific hardware features and peripherals of the target microcontroller.
Code Structure and Task Creation for Blinking LED with Switching | High-level diagram or flowchart illustrating the overall program structure & show the main function, task creation, and the main loop where context switching might occur.
Task Scheduling | How Micrium OS manages their execution.
Deployment | packaging the final build of the project & deployed to the Nucleo-F446RE board.

## Slide 3: 01 Introduction

## Slide 4: Introduction
Projcet Overview:
Goal: Port µC/OS-III on Nucleo-F446RE and develop an application that uses Micrium OS to control the switching between tasks.
Main resources used:
1) STM32 Nucleo-F446RE - Development board
2) Micrium OS (µC/OS-III)
3) Keil uVision5 IDE
4) STLINKv2 driver
5) CMSIS core for F446 family

## Slide 5: Introduction
Projcet Overview:
STM32 Nucleo-F446RE Features:
The Nucleo-F446RE is a development board based on the STM32F446RE microcontroller, which belongs to the STM32F4 series of ARM Cortex-M4-based microcontrollers.
The microcontroller is programmed using the ARM Cortex-M4 core, which supports Thumb-2 instruction set and hardware floating-point unit (FPU).

## Slide 6: Introduction
Projcet Overview:
Quick look on Micrium OS (µC/OS-III):
Micrium OS provides kernel services such as task scheduling, memory management, synchronization primitives, and inter-task communication.
Micrium OS organizes tasks as independent execution units, each with its own stack and priority level.

## Slide 7: 02 Nucleo-F446RE Setup

## Slide 8: Development Environment Setup
1)Installation of Keil uVision5
Keil uVision5 is an integrated development environment tailored for microcontroller development.
2)Setting the Toolchain
for Nucleo-F446RE
Keil uVision5 provides a package manager where we can find uitlities like the CMSIS core, the ARM compiler/linker and an STLINK hardware debugger (we have to install the STLINKv2 driver to communicate with the STLINK debug port on the Nucleo board).

## Slide 9: 03 Porting Micrium OS

## Slide 10: Configuring Micrium OS
Obtaining Micrium OS Source Code
Micrium OS source code is available for download from the official Micrium website or via package managers such as GitHub since it is an open-source project.
In this project we can find three main folders: uC_CPU , uC_LIB, uC_OS3. Each folder has a Cfg subdirectory with some configuration files we must modify to properly adapt Micrium to current device and application.
uc_cpu
uc_LIB
uc_OS3

## Slide 11: Configuring Micrium OS
Obtaining Micrium OS Source Code
Moreover, uC_CPU and uC_OS3 show two other subfolders called Templates and Ports:
In Templates folders we can find some files provided by Micrium that are meant to be completed by the developer who's porting the os. Each different device/microcontroller must have a different version of those files.
In Ports we can find some of these template files as already completed for some devices. In our case, Silicon Labs provided us the files for the STM32F446RE.
uc_cpu
uc_OS3

## Slide 12: Configuring Micrium OS
In depth explanation on porting process
uC_CPU: This folder typically contains the source code for the architecture-specific portion of Micrium OS. It provides the necessary functionalities for Micrium OS to interact with the core functionalities of the target microcontroller's CPU. During the porting process, the uC-CPU folder is essential for adapting Micrium OS to the specific CPU architecture of the target hardware platform. For this reason, multiple versions of these files are provided. In our case, we are interested in selecting ARM Cortex-M4 for STM32F446RE architecture specific files and configuration, provided by Silicon Labs.
uc_cpu

## Slide 13: Configuring Micrium OS
In depth explanation on porting process
uC_CPU: For each CPU architecture there typically three files: cpu.h, cpu_a.asm, cpu.c.
cpu.h: This file contains µC/CPU configuration specific to the processor (CPU Type) and compiler (Compiler), such as data type definitions, processor address and data word sizes, endianness word order, and critical section macros
cpu_a.asm: These (optional) file contains assembly code to enable/disable interrupts, implement critical section methods.
uc_cpu
asm

## Slide 14: Configuring Micrium OS
In depth explanation on porting process
uC_CPU:
cpu.c: This file contains C and/or assembly code to implement processor-specific code not already defined or implemented in the processor’s cpu.h (or cpu_a.asm).
uc_cpu
asm

## Slide 15: Configuring Micrium OS
In depth explanation on porting process
uC_LIB : was designed for the vast variety of embedded applications. The source code for µC/LIB is designed to be independent of and used with any processor (CPU) and compiler.
Components in this folder encompass standard C library functions, memory management utilities, string manipulation functions, and mathematical operations.
uc_LIB

## Slide 16: Configuring Micrium OS
In depth explanation on porting process
uC_LIB : The main files that are contained under µC/LIB are lib_cfg.h config file, and µC/LIB source files which are lib_ascii.c, lib_math.c, lib_mem.c, lib_str.c.
lib_cfg.h: Can be customized to enable or disable specific features of the library according to the application requirements. Configuration include settings related to memory management, string manipulation, mathematical functions, and ASCII character handling. By adjusting configurations in lib_cfg.h, developers the behavior and functionality of the µC/LIB can be tailored.
uc_LIB
asm

## Slide 17: Configuring Micrium OS
In depth explanation on porting process
uC_LIB :
lib_ascii.c: This file contains implementations of ASCII character manipulation functions. These ASCII manipulation functions are essential for processing character data in the application.
lib_math.c: This file contains implementations of mathematical functions and operations commonly used.
lib_mem.c: This file contains implementations of memory management functions for allocating, deallocating, and manipulating memory blocks.
uc_LIB
asm

## Slide 18: Configuring Micrium OS
In depth explanation on porting process
uC_LIB :
lib_ascii.c: This file contains implementations of string manipulation functions for handling character strings.
uc_LIB
asm

## Slide 19: Configuring Micrium OS
In depth explanation on porting process
uC_OS3 : This folder serves as the foundation for adapting Micrium OS to the target hardware.
uC_OS3_develop contains the core components of Micrium OS, including the kernel, task management, synchronization primitives, and inter-task communication mechanisms.
uC_OS3_develop contains the core source code for the Micrium OS kernel, this kernel provides the fundamental functionalities for building multitasking embedded systems applications.
uc_OS3

## Slide 20: Configuring Micrium OS
In depth explanation on porting process
uC_OS3 : Here we can find a set of configuration files that heavily affect the capabilities and features of the specific application we are going to run on Micrium: these are os_app_hooks.c, os_app_hooks.h, os_cfg.h, os_cfg_app.h.
There are also some utilities files containing macro functions providing asm implementation of context switching mechanisms, and the OS_CPU_SysTickHandler() function that feeds the main os clock, the SysTick, directly driven by the processor clock. These files are provided by Silicon Labs.
uc_OS3
asm

## Slide 21: Configuring Micrium OS
In depth explanation on porting process
Since an abstraction of the hardware is already provided to the os, our goal is to configure the peripherals of the microcontroller (RCC, NVIC, timers, LED ecc.) to make the os run our application.
In particular, the system needs a SysTick to schedule the tasks. The OS_CPU_SysTickHandler() function provided by Silicon Labs expects to be called when the processor clock performs a certain number of ticks, in a way that sets the SysTick frequency value to the one specified in os_cfg_app.h.

## Slide 22: Configuring Micrium OS
In depth explanation on porting process
This operation is performed by BSP_OS_TickInit() function in the bsp_os.c file, written by us.
Also BSP_OS_TickEnable() and BSP_OS_TickDisable() functions were implemented by us, using the utilities from cpu.h file.
The BSP_OS_TickISR() (which calls OS_CPU_SysTickHandler) and OS_CPU_PendSVHandler() (used during context switching) functions were already implemented, but not connected to the NVIC array. bsp_os_a.asm, written by us, covers this issue.

## Slide 23: 04 Code Structure

## Slide 24: program flow and structure
Header Inclusions
The code includes headers such as:
core_cm4.h: ARM Cortex-M4 core definitions.
os.h: The RTOS header, defining the kernel's API.
Other headers for board support package (BSP), application configuration
(app_cfg.h), and peripherals like LEDs and buttons.
Task Control Blocks (TCBs)
Task Control Blocks (TCBs) for various tasks:
start_tsk_tcb: TCB for the start task.
led1_tcb: TCB for the LED1 task.
led2_tcb: TCB for the LED2 task.

## Slide 25: program flow and structure Cont.
Task Stacks
Mutexes and Timers
Each task is allocated a stack, defined as arrays of CPU_STK_SIZE:
start_tsk_stack: Stack for the start task.
led1_tsk_stack: Stack for the LED1 task.
led2_tsk_stack: Stack for the LED2 task.
mutex: A mutex object is defined, likely for synchronizing shared resources between tasks.
timer: A software timer (OS_TMR), with a callback function.

## Slide 26: program flow and structure Cont.
Function Prototypes
The main tasks and utilities are declared:
start_task(void *p_arg): The main start task.
led1_task(void *p_arg): Task to control LED1.
led2_task(void *p_arg): Task to control LED2.
TimerCallback(void *p_tmr, void *p_arg): Timer callback function.
Delay(uint32_t dlyTicks): A delay utility.

## Slide 27: program flow and structure Cont.
Main Function
The main function is responsible for initializing the system:
Initialization:
  BSP_Init(): Initializes the board support package.
  CPU_IntDis(): Disables interrupts during initialization.
  CPU_Init(): Initializes the CPU for handling interrupts.
  LED_Initialize() and Buttons_Initialize(): Initializes the LED and
  button peripherals.
After starting the OS, the main() function enters an infinite loop:
while(DEF_ON): This loop should never be executed, as the OS takes control once OSStart() is called.

## Slide 28: program flow and structure Cont.
RTOS Initialization
OSInit(&err): Initializes the RTOS. This function sets up the kernel and prepares the system for multitasking, but does not start it yet.

## Slide 29: program flow and structure Cont.
Task Creation
start task will be responsible for creating other tasks.
OSTaskCreate(): This function creates a task and adds it to the OS scheduler. The parameters include:
  start_tsk_tcb: The TCB (Task Control Block) for the start task.
  "start task": The name of the task.
  start_task: The function that implements the task logic.
  0: The argument passed to the task (unused here).
  APP_CFG_TASK_PRIO: The task priority.
  start_tsk_stack: The stack for the task.
  Stack size and other options.
Once the start task is created, the OS can be started:
OSStart(&err): This function starts the multitasking. From this point, the control is handed over to the RTOS, and tasks will be scheduled according to their priorities and the RTOS configuration.

## Slide 30: program flow and structure Cont.
Start Task
The start_task() function performs further system setup:
BSP_OS_TickEnable(): Enables the tick timer for the OS, which was initially disabled.
OSSchedRoundRobinCfg(): Configures Round Robin scheduling, allowing tasks to share CPU time equally, with a time slice of 6000 ticks.
OSMutexCreate(): Creates a mutex, which will be used for synchronizing access to shared resources between tasks.
The context switching occurs during the OS's scheduling phase, after the call to OSStart(). The RTOS will switch between tasks based on their priorities, whether they are ready to run, and according to the configured Round Robin scheduling.

## Slide 31: program flow and structure Cont.
Additional Task Creation
After the start_task, other tasks are created:
led1_task and led2_task are created using OSTaskCreate(), similar to the start_task.
The parameters include:
  Task Control Block (TCB), task name, task function, priority, stack, and options.
Timer Setup
OSTmrCreate(): Creates a software timer with a periodic callback (TimerCallback), which is set to trigger every 4 ticks.
OSTmrStart(): Starts the timer, allowing it to run and invoke the callback at each period.

## Slide 32: program flow and structure Cont.
Task Implementations
led1_task(): This task enters an infinite loop (while (DEF_TRUE)) and repeatedly turns an LED on and off with a 200ms delay between states. The specific LED controlled is determined by blnk_LED.
led2_task(): Similar to led1_task, this task toggles an LED on and off with a 400ms delay.

## Slide 33: program flow and structure Cont.
Context Switching
The RTOS handles context switching between tasks once the OS is started via OSStart().
Tasks such as led1_task and led2_task will share CPU time according to the Round Robin scheduling (OSSchedRoundRobinCfg()), meaning each task gets a fixed time slice to run before the OS switches to another task.
The timer interrupt will also cause context switches as it triggers the TimerCallback function.

## Slide 34: 05 Tasks Structure

## Slide 35: Tasks structure
Task Control Blocks (TCBs):
Code Snippet:
/* Definition of the Task Control Blocks for three tasks */
static OS_TCB start_tsk_tcb;
static OS_TCB led1_tcb;
static OS_TCB led2_tcb;
The TCB is essential for the RTOS to manage task states, priorities, stack pointers, this structure is of type OS_TCB. Other task-specific data :-
Task Name
Task Time Quanta
Message Queue
Event Wait List
Task Delay
Mutex Nesting Level
Task CPU Usage

## Slide 36: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
OS_ERR err;
This variable (err) is of type OS_ERR, is used by to store error codes that result from various OS operations.
Code Snippet:
BSP_Init();
CPU_IntDis();
CPU_Init();
The BSP_Init() function is responsible for initializing the Board Support Package (BSP).The CPU_IntDis() function is used to disable all CPU interrupts globally. The CPU_Init() function initializes the CPU and any CPU-specific features or resources.

## Slide 37: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
LED_Initialize();
Buttons_Initialize();
‘LED_Initialize()’ Responsible for initializing the LEDs on the hardware, involves configuring the GPIO pins connected to the LEDs as output pins and setting an initial state.
‘Buttons_Initialize()’ is responsible for configuring the hardware buttons on the system. Which is setting the corresponding GPIO pins as inputs.

## Slide 38: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
OSInit(&err);
The OSInit() function initializes the operating system . It sets up all necessary internal data structures, initializes kernel, timers, and semaphores, and prepares the OS for task scheduling. After calling OSInit(), the RTOS is ready to start creating and managing tasks.
Kernel Data Structures: Initializes the internal data structures required by the RTOS, such as task control blocks (TCBs), ready lists.
‘Task Management: Sets up the task management system, including the creation of idle tasks.
Error Handling: The err parameter captures any errors that occur during the initialization process.

## Slide 39: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
OSTaskCreate(…);
This function creates and initializes a task in the RTOS. which will be responsible for further system initialization and creating other tasks.
OS_TCB *start_tsk_tcb: A pointer to the Task Control Block (TCB) for the start task.
CPU_CHAR *"Start Task": A string representing the task name.
OS_TASK_PTR start_task: A pointer to the task function that will be executed (start_task()).
void *0: A pointer to any arguments passed to the task. In this case, no arguments are passed, so it’s set to 0.

## Slide 40: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
OSTaskCreate(…);
OS_PRIO APP_CFG_TASK_PRIO: The priority of the task. The priority determines the order in which tasks are scheduled. The value is defined in app_cfg.h.
CPU_STK *start_tsk_stack[0]: A pointer to the stack allocated for the task.
CPU_STK (APP_CFG_TASK_STK_SIZE / 10u): Specifies the stack’s limit , which helps with stack overflow detection.
CPU_STK_SIZE APP_CFG_TASK_STK_SIZE: The size of the stack for this task, defined in app_cfg.h.
OS_MSG_QTY 0: The number of messages the task can handle, which is 0 in this case since it doesn’t use a message queue.

## Slide 41: Tasks structure – cont.
Detailed Breakdown of main():
Code Snippet:
OSTaskCreate(…);
OS_TICK 0: The time slice allocated to the task, which is set to 0, indicating no time slicing.
void *0: Additional options passed to the task, which is NULL here.
OS_OPT (OS_OPT_TASK_STK_CHK | OS_OPT_TASK_STK_CLR): Enable stack checking and clearing, which help in debugging and stack overflow detection.
OS_ERR *err: A pointer to the error code that will indicate if the task creation was successful or not.

## Slide 42: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
static void start_task(void *p_arg){…} [1]
BSP_OS_TickEnable(); [2]
[1] The function start_task is the entry point for the initial task that runs when the system starts.
[1] p_arg: This parameter allows the task to receive an argument when it is created. However, in this case, it is not used, so (void)p_arg is a common way to prevent compiler warnings about unused parameters.
[2] This function enables the OS tick timer and the corresponding interrupt.as it provides the periodic "ticks" that the OS uses to keep track of time and manage task scheduling. This call re-enables the tick timer after the system initialization is complete.

## Slide 43: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSSchedRoundRobinCfg(…) [1]
[1] This configures the RTOS's round-robin scheduling. Round-robin scheduling allows tasks of the same priority to share the CPU by switching between them at regular intervals.
DEF_TRUE: Enables round-robin scheduling.
6000u: Specifies the number of OS ticks that each task will run before the OS switches to the next task in the round-robin pool. In this case, a task will run for 6000 ticks before being switched out.
Error Handling: The result of this configuration is stored in the err variable, which can be checked later to ensure that the operation was successful.

## Slide 44: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSMutexCreate(…) [1]
[1] Creates a mutex (mutual exclusion object) which can be used by tasks to ensure exclusive access to shared resources.
&mutex: A reference to the global OS_MUTEX variable that holds the mutex object.
"mutex": A human-readable name for the mutex, useful for debugging purposes.
Error Handling: Again, the err variable is used to check whether the mutex creation was successful.

## Slide 45: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSTaskCreate(…) [1]
[1] This creates the led1_task, which is one of the tasks that will run concurrently in the system.
Task Control Block (TCB): The &led1_tcb is a pointer to the TCB for the task.
Task Name: The string "led1 task" is the name of the task.
Priority: APP_CFG_L1_TASK_PRIO is the priority assigned to this task. The lower the number, the higher the priority.
Stack: The stack for this task is defined by &led1_tsk_stack[0], and its size is set by APP_CFG_TASK_STK_SIZE.
Options: OS_OPT_TASK_STK_CHK | OS_OPT_TASK_STK_CLR specifies options to check and clear the task stack.
Error Handling: The err variable captures the success or failure of the task creation.

## Slide 46: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSTaskCreate(…) [1]
[1] Create the LED2 Task : Similar to the led1_task, this creates the led2_task, which is another task that will run concurrently in the system.
TCB, Stack, Priority: The same concepts apply as with the led1_task, but here it uses led2_tcb, led2_task, and APP_CFG_L2_TASK_PRIO for the task control block, task function, and priority, respectively.

## Slide 47: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSTmrCreate(…) [1]
[1] This creates a periodic timer that will trigger every 4 ticks. The timer will call the TimerCallback function each time it expires.
Timer Object: The timer is referenced by the &timer object.
Timer Name: "timer" is the name of the timer for debugging purposes.
Timer Period: The timer starts at 0 ticks and will repeat every 4 ticks.
Options: OS_OPT_TMR_PERIODIC sets the timer to be periodic, meaning it will keep repeating until explicitly stopped.
Callback: The TimerCallback function is called each time the timer expires.
Error Handling: The err variable captures any errors during timer creation.

## Slide 48: Tasks structure – cont.
Detailed Breakdown of start_task(…):
Code Snippet:
OSTmrStart(&timer, &err); [1]
[1] Purpose: This starts the previously created timer. Once started, the timer will begin counting ticks and will call the TimerCallback function periodically.
Error Handling: The err variable captures any errors that occur when starting the timer.

## Slide 49: Tasks structure – cont.
Detailed Breakdown of led1_task & led2_task:
Code Snippet:
static void led1_task (void *p_arg) {…}
static void led2_task (void *p_arg) {…}
The two tasks led1_task and led2_task in the provided code are responsible for controlling the behavior of LEDs. Both tasks run in an infinite loop and toggle the state of a specified LED, but with different timing intervals.
The led1_task is responsible for blinking an LED with shorter on and off intervals. It continuously toggles the LED on and off, with each state lasting for 200 ticks.
Key Elements: Infinite Loop (while (DEF_TRUE)): This ensures that the task runs continuously, as tasks in a real-time operating system typically do not exit. DEF_TRUE is a constant that equates to 1, making the condition always true.

## Slide 50: Tasks structure – cont.
Detailed Breakdown of led1_task & led2_task:
Code Snippet:
static void led1_task (void *p_arg) {…}
static void led2_task (void *p_arg) {…}
LED_On(blnk_LED): This function turns on the LED specified by blnk_LED. The blnk_LED variable likely refers to a particular LED that has been set elsewhere in the code.
Delay(200): The task waits for 200 ticks after turning on the LED. The Delay function introduces a pause in the task, during which the RTOS can switch to other tasks.
LED_Off(blnk_LED): This function turns off the specified LED.
Delay(200): The task waits for another 200 ticks after turning off the LED.
Timing: The total cycle time for this task (on + off) is 400 ticks, meaning the LED will blink with a period of 400 ticks (200 ticks on, 200 ticks off).

## Slide 51: 06 Deployment

## Slide 52: Sequence
Board Setup
Porting
Devlopment
Building
Release
ELF

## Slide 53: Resources
https://micrium.atlassian.net/wiki/spaces
https://github.com/weston-embedded/uC-OS3

## Slide 54: Thanks!
Credits
Mohamed Hossam
Gino Fachechi